## Slide 1
Registers
<1 KB · ~0.3 ns
L1 Cache
32 KB · ~1 ns
L2 Cache
256 KB · ~4 ns
L3 Cache
6 MB · ~12 ns
DRAM
>8 GB · ~60–80 ns
Memory Hierarchy
Cache & Locality
Performance Lab
Mid-term Project Technical Presentation
Computer Systems | Istanbul Atlas University | April 2026
Team 11
Ebru Inci Dhafer Hamza Sfaxi
Kasra Nikdel Fadi Ibrahim Basha

## Slide 2
Project Overview & Agenda
Overview
01
Methodology
Timer infrastructure · CLOCK_NOW macro · clock_gettime(CLOCK_MONOTONIC) · platform notes for Apple Silicon
02
Stride Access
How cache-line granularity controls per-access latency
03
Working Set Size
Latency step transitions across L1 → L2 → L3 → DRAM
04
Matrix Traversal
Row-major vs column-major: spatial locality and slowdown ratio
05
Pointer Chasing
Random linked-list hops that defeat hardware prefetching
06
Memory Bandwidth
Copy vs sum kernels · peak GB/s by cache level · serial dependency bottleneck
07
Key Findings
Five practical rules derived from measured data
Five benchmark modules · C11 · gcc -O2 · Apple Silicon M-series

## Slide 3
Methodology — Timer & Benchmark Architecture
Methodology
Core Timing Primitive — src/timer.h
/* timer.h — POSIX clock_gettime wrapper */
#include <time.h>
static inline double timespec_diff_ns(
const struct timespec *t0,
const struct timespec *t1) {
return (double)(t1->tv_sec - t0->tv_sec)*1e9
+ (double)(t1->tv_nsec - t0->tv_nsec);
}
#define CLOCK_NOW(ts) clock_gettime(CLOCK_MONOTONIC,&(ts))
/* Usage in each benchmark: */
double best_ns = 1e18;
for (int iter = 0; iter < BENCH_ITERS; iter++) {
struct timespec t0, t1;
CLOCK_NOW(t0);
/* ... benchmark kernel ... */
CLOCK_NOW(t1);
double ns = timespec_diff_ns(&t0,&t1) / n;
if (ns < best_ns) best_ns = ns;
}
Why best-of-5?
OS scheduling, page faults, and thermal events produce upward outliers. The minimum timer value represents the hardware latency floor without software noise.
Why divide by n_accesses?
Measures per-operation cost, not total elapsed time. Allows fair comparison across experiments with different loop counts.
Platform: Apple Silicon
UMA architecture, ~8-16 MB System Level Cache, LPDDR bandwidth >100 GB/s, aggressive hardware prefetcher. Results differ predictably from x86 textbooks.
Project Source Layout
src/ timer.h config.h main.c
stride_bench.c workingset_bench.c
matrix_bench.c linkedlist_bench.c bandwidth_bench.c
Build & Run
$ make # builds all five benchmarks
$ make run # runs + writes results/*.csv
$ gcc -O2 -std=c11 -Wall -Wextra src/*.c -o cache_lab
Compiler: gcc -O2 -std=c11 -Wall -Wextra · BENCH_ITERS=5 · MIN_ACCESSES=4,000,000

## Slide 4
Experiment 1 — Stride Access Pattern
Stride
Cache-Line Boundary
64-byte cache lines are the atomic unit of data transfer. On Apple Silicon the prefetcher hides the 64B boundary — the latency spike appears at 128 bytes (two consecutive lines).
Measured Results
4–64 B stride: ~0.88 ns (L1 hit)
128 B stride: 4.50 ns ★ spike!
256+ B: 1.6–3.8 ns (stream)
Benchmark Kernel — stride_bench.c
for (long long i = 0; i < SIZE; i += stride_elems)
sum += arr[i]; // touches a new 64-B cache line
// whenever stride_bytes >= 64
// volatile sink prevents dead-code elimination:
volatile long long _sink = sum;
Hardware: What Triggers a Cache Miss?
The CPU loads memory in 64-byte blocks (cache lines). Two accesses to the same line cost only one fetch. Apple M-series prefetches pairs of lines (128 B window), so the spike shifts from the expected 64 B to 128 B — only a stride that crosses both lines in the prefetch pair causes a guaranteed miss. Padding hot structs to 64-byte boundaries prevents false sharing across cores.
Experiment 1: 64 MB int array · strides swept 1–1024 elements · ~0.88 ns (hit) vs ~4.5 ns (miss)

## Slide 5
Experiment 2 — Working Set Size
Working Set
Expected vs Observed
Expected (x86):
4-step latency profile
L1→L2→L3→DRAM
Observed (M-series):
Flat ~1 ns across
all array sizes
Why the flat curve?
① Aggressive HW prefetcher recognises sequential scans
② ~8-16 MB System Level Cache absorbs medium arrays
③ LPDDR bandwidth >100 GB/s serves large arrays fast
Sequential Scan Kernel — workingset_bench.c
// Scan the entire working set once per iteration
long long sum = 0;
for (long long i = 0; i < n_elems; ++i)
sum += arr[i]; // stride = 4 B (int)
// HW prefetcher detects stride=1 and issues
// the NEXT cache line BEFORE the CPU asks for it
x86 vs Apple Silicon — Why the Curve Differs
x86 (Intel/AMD): prefetcher covers only L1/L2. Arrays larger than L2 still show a step increase at the L3/DRAM boundary because the prefetcher cannot hide L3 misses.
Apple M-series: the System Level Cache (SLC, ~8–16 MB) is private to the CPU cluster and sits between L3 and DRAM. It absorbs medium-size sequential arrays entirely, collapsing the expected 4-step profile to a flat ~1 ns line.
Experiment 2: array sizes 1 KB – 256 MB · sequential scan · Apple Silicon hides all transitions

## Slide 6
Experiment 3 — Matrix Traversal Order
Matrix
Slowdown Summary
Matrix Size Slowdown
N=64 32 KB 1.09×
N=256 512 KB 1.47×
N=1024 8 MB 1.45×
N=4096 128 MB 1.53×
Key Insight
Observed 1.5× vs theoretical 8× max. The hardware prefetcher detects the regular column stride and partially compensates — but the penalty remains real and consistent.
The Critical Difference — matrix_bench.c
// ✓ Row-major — cache-friendly (stride = 8 B / double)
for (int i=0;i<N;++i)
for (int j=0;j<N;++j) s += m[i][j];
// ✗ Col-major — cache-hostile (stride = N×8 B)
for (int j=0;j<N;++j)
for (int i=0;i<N;++i) s += m[i][j]; // 1.5× slower!
Spatial Locality & C Memory Layout
C stores 2-D arrays in row-major order: m[0][0], m[0][1], m[0][2] … are adjacent bytes in memory. Row-major access walks through contiguous memory — each 64-byte cache line holds 8 doubles and all 8 are used.
Column-major access jumps N×8 bytes between iterations. For N=1024 that is 8 KB per step — one cache miss per element. The theoretical max slowdown is 8× (one double per line); we measured 1.5× because the HW prefetcher partially compensates.
Experiment 3: N×N double matrices, N=64–4096 · col-major is always slower · write cache-friendly loops

## Slide 7
Experiment 4 — Pointer Chasing (Linked List)
Pointer Chasing
Latency by Cache Level
≤128 KB ~0.65 ns
L1/L2
256 KB ~4 ns
L2→L3
512K–16MB ~8–11 ns
L3
32 MB ~38 ns
→DRAM
≥64 MB ~70–83 ns
DRAM
128× latency range from L1 to DRAM. Pointer chasing serialises loads — the CPU cannot prefetch the next address until the current load completes.
Node Struct & Chase Loop — linkedlist_bench.c
struct __attribute__((aligned(64))) Node {
struct Node *next;
char pad[56]; /* 1 node = 1 cache line */
};
// Fisher-Yates shuffle with srand(42) + rand()
__attribute__((noinline))
Node* chase_nodes(Node *head, long long n) {
for (Node* p = head; p; p = p->next);
__asm__ volatile("" ::: "memory"); /* barrier */
}
Why Hardware Prefetching Cannot Help
The address of the next node is stored inside the current node — which has not been loaded yet. This creates a load-use dependency: the CPU cannot issue the next memory request until the current one completes. Each hop is a fully serialised cache miss.
alignas(64) guarantees that every node occupies exactly one cache line, so each hop always fetches a fresh 64-byte block. The __attribute__((noinline)) + asm volatile barrier was essential to prevent the compiler from eliminating the loop at -O2.
Experiment 4: Fisher-Yates shuffled list · alignas(64) nodes · __attribute__((noinline)) + asm volatile barrier

## Slide 8
Experiment 5 — Memory Bandwidth
Bandwidth
Peak Copy Bandwidth
Level Copy Sum
L1 (~8 KB)
253 GB/s
17.2 GB/s
L2 (~256 KB)
168 GB/s
17.2 GB/s
L3 (~8 MB)
89 GB/s
17.2 GB/s
DRAM (>64MB)
109 GB/s
17.1 GB/s
Why is sum always ~17 GB/s?
Serial FP-add dependency chain: each iteration s += src[i] must wait for the previous addition (~5 cycle latency at 3.5 GHz). Memory bandwidth is completely irrelevant.
Two Kernels, Two Bottlenecks — bandwidth_bench.c
// Copy — independent, bandwidth-limited:
for (long long i=0; i<n; ++i) dst[i]=src[i];
// Sum — SERIAL dependency on 's' (compute-limited):
double s = 0;
for (long long i=0; i<n; ++i) s += src[i];
// each iter WAITS for prev FP-add to finish (~5 cyc)
The Serial Dependency Bottleneck Explained
Copy issues independent load/store pairs — the CPU can pipeline many at once and the bottleneck is purely memory bandwidth (>100 GB/s on Apple Silicon).
Sum carries a loop-carried dependency: s_{i+1} = s_i + src[i]. The FP-add unit has ~5-cycle latency, so only one addition completes per 5 cycles. At 3.2 GHz: 4 B ÷ (5 cycles ÷ 3.2 GHz) ≈ 2.6 GB/s theoretical ceiling. Measured 17 GB/s means the compiler auto-vectorised with partial unrolling — but it still cannot reach memory-speed.
Experiment 5: copy (read+write) vs sum (read-only) · DRAM copy 109 GB/s · sum bottlenecked by compute, not memory

## Slide 9
Results Dashboard — All Experiments at a Glance
Dashboard
Exp 1 — Stride Access
Exp 2 — Working Set
Exp 3 — Matrix Traversal
Exp 5 — Memory Bandwidth
Dashboard: Stride · Working Set · Matrix Slowdown · Bandwidth · all data from live benchmarks on Apple Silicon

## Slide 10
Key Findings — Five Practical Rules
Findings
1
Cache-line granularity is real
Accesses spaced >64 bytes apart each require a new 64-byte fetch. Pad hot data structures to align with cache-line boundaries to avoid wasting bandwidth.
struct __attribute__((aligned(64))) HotData { int x, y, z, pad[13]; };
2
Sequential access is nearly free on Apple Silicon
Prefetching + SLC hides the memory hierarchy for sequential scans. On x86 the 4-tier latency penalty is fully visible at each cache boundary.
for (size_t i=0; i<n; ++i) sum+=arr[i]; // stride=1 → prefetch wins
3
Write row-major loops
Column-major traversal is 1.5× slower on M-series and up to 8× on x86. Always let the innermost loop index advance the last (column) dimension.
for(i) for(j) s+=m[i][j]; // ✓ vs for(j) for(i) s+=m[i][j]; // ✗
4
Pointer chasing forces full memory latency
128× gap between L1 (0.65 ns) and DRAM (83 ns). Each hop is serialised — the CPU cannot prefetch the next address until the current load completes.
// Prefer arr[idx[i]] over p=p->next when list fits in cache
5
High bandwidth ≠ high performance
Serial loop-carried dependencies (prefix-sum, reductions) are CPU-latency-bound. Breaking the chain with multiple accumulators recovers throughput.
double s0=0,s1=0; s0+=a[2*i]; s1+=a[2*i+1]; // break dep chain
All findings supported by live benchmark data collected on Apple Silicon M-series · C11 · gcc -O2

## Slide 11
Conclusions
Memory access pattern is a first-order performance variable — often more impactful than algorithm choice.
Platform architecture determines which memory hierarchy effects are visible. Apple Silicon hides effects that x86 exposes.
Benchmarking requires careful implementation: noinline, volatile sinks, and compiler barriers prevent dead-code elimination.
The 128× latency range from L1 to DRAM underlines the value of keeping hot data in cache.
Memory bandwidth only helps when the algorithm structure can exploit it; serial dependencies override it.
Thank You
Cache & Locality Performance Lab
Computer Systems · Istanbul Atlas University · April 2026
Team 11
Ebru Inci Dhafer Hamza Sfaxi
Kasra Nikdel Fadi Ibrahim Basha
Questions?